## Slide 1
SPI
PROJECT
SPI

## Slide 2
Mădălina Mihălucă
Alexandru Antoci
Andrei Popa
Student
Student
Student
Our team
Silicon Service

## Slide 3
Table of Contents
  What is a SPI
  About Vivado
  About Verilog
  Vivado Workflow
  Block Diagram
  Internal Structure
  Basys 3Board
  Block Diagram
  Internal Structure
  Simulation Waveform
  Code
  Bibliography

## Slide 4
SPI, or Serial Peripheral Interface, is a communication protocol used to transfer data between a microcontroller and peripheral devices. It enables fast, synchronous data exchange using four main signals:
WHAT IS A SPI?
MOSI (Master Out Slave In): Sends data from the master device to the slave.
MISO (Master In Slave Out): Sends data from the slave device back to the master.
SCK (Serial Clock): Provides the clock signal from the master to synchronize data transfer.
SS/CS (Slave Select/Chip Select): Selects the slave device that the master communicates with.

## Slide 5
SPI
Real World Applications of
In Engineering

## Slide 6
Gaming consoles
The PlayStation 5's DualSense controller utilizes SPI to relay data from the controller to the console, enabling responsive haptic feedback and adaptive trigger functionalities.
Smartphones
SPI is commonly used to connect the main processor with various peripherals such as touchscreens, fingerprint sensors, and memory modules.

## Slide 7
Smart home Devices
Smart home devices also benefit from SPI's robust communication capabilities. Smart thermostats, security cameras, and home automation hubs often use SPI to facilitate communication between the central processor and various peripheral components.

## Slide 8
Vivado is a software program developed by Xilinx for designing and programming programmable logic circuits, such as FPGAs. It is used by engineers to create, simulate, verify, and implement complex digital designs on hardware.
The main languages supported by Vivado are: VHDL, Verilog, SystemVerilog, C/C++.
About
Used for FPGA Design and Implementation
Used for Embeded Systems
Vivado

## Slide 9
Implementation
Synthesis
Generate Bitstream
Open Hardware
manager
Simulation
This step includes placing and routing the circuit generated by synthesis, ensuring that the design aligns with the available hardware resources.
Synthesis identifies synthesis errors and transforms the design described in a hardware description language into a concrete physical circuit. .
Simulation means testing and verifying the digital design, without actually building the physical circuit, to ensure it functions as expected before its real-world implementation.
Generate Bitstream refers to the process of creating a bitstream file from a hardware design, which is then used to program a programmable logic device such as an FPGA.
VIVADO WORKFLOW
This step establishes the connection to the hardware resource, in our case, the Basys 3 FPGA.

## Slide 10
Verilog is a hardware description language used to model and simulate digital circuits. It is widely used in the development of integrated systems and FPGA design.
VERILOG
We have chosen to implement the project using the Verilog.
Verilog allows for the description of both the behavior and the structure of circuits, providing a way to describe and simulate the circuit before physically implementing it.
VERILOG

## Slide 11
Data in
Master
Power
Button
Data out
Master
Data out
Slave
Data in
Slave
Pl
Reset
Ready
state
BASYS 3 BOARD

## Slide 12
BLOCK DIAGRAM

## Slide 13
MASTER INTERNAL STRUCTURE

## Slide 14
SIMULATION WAVEFORM

## Slide 15
C
o
u
n
t
e
r

## Slide 16
S
h
i
f
t
R
e
g
i
s
t
e
r

## Slide 17
FSM
master

## Slide 18
BIBLIOGRAPHY
https://forum.digikey.com/t/implementing-a-robust-microcontroller-to-fpga-spi-interface-part-2-protocol-definition
https://www.fpga4student.com/p/fpga-projects.html
https://www.xilinx.com/products/boards-and-kits/1-54wqge.html
https://chatgpt.com

## Slide 19
HANK YOU